## Slide 1
Singularity-Aware Physics-Informed
Neural Networks for Real-Time
Inverse Kinematics
Safe, Real-Time Motion Control for Robot Arms Using AI
BY Group 18:
Team Member 1 Roll No: __________
Team Member 2 Roll No: __________
Team Member 3 Roll No: __________
Team Member 4 Roll No: __________

## Slide 2
Introduction
Robot arms are used in factories, hospitals, warehouses, and space missions.
To move the arm's hand to a target point, we must find the correct angle for every joint.
This calculation is called Inverse Kinematics (IK).
Modern arms have 7 joints — more than the minimum needed — which makes this calculation harder.
Target Point
(a location in space)
Joint Angles
(7 angles, one per joint)
Inverse Kinematics = solving this direction

## Slide 3
Key Terms
1
Forward Kinematics
Know the joint angles → calculate where the hand ends up. (The easy direction.)
2
Inverse Kinematics
Know where we want the hand → find the joint angles. (The hard direction.)
3
Redundant Arm
An arm with extra joints — many different angle combinations reach the same point.
4
Singularity
A risky arm position where the controller can suddenly demand impossibly fast joint movement.

## Slide 4
Motivation
Classical methods can freeze, or move dangerously fast, near singularities.
This risks damaging expensive robots or harming people working nearby.
Extra joints mean many solutions exist — plain AI models often blend them into nonsense.
A fast, self-checking AI solver could let robots react safely in real time.

## Slide 5
Problem Statement
Robot arms can freeze or move dangerously fast when they reach certain risky joint positions, called singularities. Classical control methods struggle to handle these safely — especially in arms with extra joints, which have many possible solutions for reaching the same target point.
NEED A fast, learning-based method is needed that can reach a target position while automatically staying away from these risky positions — without needing a large labeled dataset to train on.

## Slide 6
Literature Review
Author(s) | Title | Journal | Outcomes | Limitations
Aydogmus & Boztas (2024) [1] | Singularity-free IK for humanoid arm via Bayesian-optimized DNN | Measurement, vol. 229 | High accuracy (MAE 0.02); 25ms predictions | Needs ~10B training samples; no explicit singularity-avoidance loss
Deng et al. (2024) [2] | Physics-informed ML model for inverse dynamics in robotic manipulators | Applied Soft Computing, vol. 163 | Physics-informed network improves torque prediction on a 7-DOF arm | Solves inverse dynamics (torque), not kinematics; no singularity handling
Calzada-Garcia et al. (2025) [3] | Review: IK, control & planning for manipulators via DNNs | Algorithms, vol. 18 | Surveys 5 years of DNN-based IK methods | Review only — no new singularity-safe solver proposed
Shi et al. (2021) [4] | Kinematics and singularity analysis of a 7-DOF redundant manipulator | Sensors, vol. 21 | Closed-form singularity conditions for a 7-DOF arm | Purely analytical; no learning-based real-time solver
Hong, Li & Huang (2024) [5] | RL-enhanced pseudo-inverse for self-collision avoidance of redundant robots | Frontiers in Neurorobotics, vol. 18 | 99.72% success avoiding self-collision on a 7-DOF Franka Panda | Targets self-collision, not singularity / manipulability safety

## Slide 7
Gaps in Literature
Most learning-based IK methods have no explicit rule to avoid singularities.
Physics-informed learning has been used for torque prediction, not singularity-safe kinematics.
Classical singularity analysis is accurate but not learning-based or adaptive.
No reviewed work combines all three — training, joint limits, and singularity safety — in one model.

## Slide 8
Objectives
1
Build the Simulated Arm
Create a computer model of a 7-joint robot arm that can be learned from.
2
Design the AI Model
Build a neural network that predicts safe joint movements.
3
Teach Three Safety Rules
Reach the target, respect joint limits, and avoid risky positions.
4
Compare With Tradition
Benchmark the AI model against a classical numerical solver.
5
Test and Fix
Find and fix real problems uncovered during training.

## Slide 9
Our Approach
Target
Point
AI Model
(uses current pose)
Predicted
Joint Angles
Safety
Check
Safe Arm
Movement
The AI looks at where the arm is right now, then predicts a small, safe movement toward the target — instead of guessing a brand-new pose from scratch.

## Slide 10
How We Keep It Safe
1
Reach the Target
The predicted hand position should end up close to the goal point.
2
Respect Joint Limits
No joint should twist past its safe mechanical range.
3
Avoid Risky Positions
The AI is discouraged from moving into “locked”, high-risk configurations.

## Slide 11
What We Built So Far
A simulated 7-joint robot arm (Franka Panda) that a computer can move and measure
A traditional (classical) solver, used as a fair comparison baseline
The AI model itself — the physics-informed neural network
A training system that generates its own practice examples — no manual dataset needed
A testing and comparison system to measure accuracy and safety

## Slide 12
Testing & Debugging
We didn’t just build it — we tested it and found real problems.
1
Problem 1
A math error in how arm sensitivity was calculated — caught by cross-checking against an independent method, then fixed.
2
Problem 2
Some training examples asked the AI to do something physically impossible for it — found by analyzing results, then fixed.
3
Problem 3
The “avoid risky positions” rule was barely active because its safety threshold was set too strictly — found and fixed.

## Slide 13
Preliminary Results: Training Progress
Chart: How Far the Predicted Hand Is From the Target, Over Training
| 1 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000
Position error (mm) | 145.44 | 98.97 | 72.41 | 59.68 | 55.64 | 49.32 | 44.5 | 42.96 | 40.06 | 40.1 | 40.2
Error dropped steadily and kept improving as training continued (10,000 steps shown).

## Slide 14
Preliminary Results: AI vs Traditional Method
Chart: Distance to Target (mm) lower is better
| Our AI Model | Classical Method
Distance to target (mm) | 32.69 | 0.47
Chart: Safety Margin Near Risky Positions higher is safer
| Our AI Model | Classical Method
Safety margin | 0.0153 | 0.0105
Our model is already safer near risky positions — accuracy is still catching up with more training.

## Slide 15
Current Limitations & Next Steps
Accuracy still trails the traditional method — needs more training and a bigger network.
Not yet connected to a 3D physics simulator for visual demonstration.
Next: longer training runs, a bigger network, and simulator integration for a live demo.

## Slide 16
References
[1] O. Aydogmus and G. Boztas, “Implementation of singularity-free inverse kinematics for humanoid robotic arm using Bayesian optimized deep neural network,” Measurement, vol. 229, p. 114471, 2024.
[2] W. Deng, F. Ardiani, K. T. P. Nguyen, M. Benoussaad, and K. Medjaher, “Physics informed machine learning model for inverse dynamics in robotic manipulators,” Applied Soft Computing, vol. 163, p. 111877, 2024.
[3] A. Calzada-Garcia, J. G. Victores, F. J. Naranjo-Campos, and C. Balaguer, “A review on inverse kinematics, control and planning for robotic manipulators with and without obstacles via deep neural networks,” Algorithms, vol. 18, no. 1, p. 23, 2025.
[4] X. Shi, Y. Guo, X. Chen, Z. Chen, and Z. Yang, “Kinematics and singularity analysis of a 7-DOF redundant manipulator,” Sensors, vol. 21, no. 21, 2021.
[5] T. Hong, W. Li, and K. Huang, “A reinforcement learning enhanced pseudo-inverse approach to self-collision avoidance of redundant robots,” Frontiers in Neurorobotics, vol. 18, 2024.
[6] Y. Nakamura and H. Hanafusa, “Inverse kinematic solutions with singularity robustness for robot manipulator control,” Journal of Dynamic Systems, Measurement, and Control, vol. 108, no. 3, pp. 163–171, 1986.

## Slide 17
Thank You